## Slide 1
Smartphone accelerometers do not require explicit user permissions
Smartphones are often placed next to the user’s laptop or keyboard
Malicious applications can recover text by identifying signals from different keystrokes
Threat Model
Develop an infrastructure for characterizing keypress vibrations
  Captured, analyzed and built profiles of keypresses on a nearby keyboard based on the generated vibrations
  Successfully recovered words using Boosted Decision Stumps
Dataset made publicly available
  Provided noise-free signal data for each letter of the English alphabet
  Developed an infrastructure for analysis and extraction of features
Contributions
Features extracted
  mean, rms, skewness, kurtosis, variance, min, max
  Fast Fourier Transformation coefficients (30)
Classifier used: AdaBoost with Decision Stump as weak learner
Data Processing Architecture
Princeton University
Jennifer Guo Yi-Hsien Lin Akshay Mittal Wathsala Vithanage
EavesDroid: Keystroke recovery using mobile phone
accelerometers
Clipper
Signal Breaker
Feature Extractor
Supervised Learning Module
Labeled
Features
AdaBoost With Decision Stump
Labeler
Clipper
Signal Breaker
Feature Extractor
Features
Trained AdaBoost With Decision Stump
Dictionary With Keyboard Features
(L/R) (U/D)
Prediction Output
Learning Phase
Attack Phase
Phone
Feature Extractor
Keystrokes
L/R Classifier
U/R Classifier
Word Profile
Feature Matching
Word
Dictionary
“juice”
1=<x,y,z>
2=<x,y,z>
…
5=<x,y,z>
1=FV-1
2=FV-2
…
5=FV-5
1=FV-1
2=FV-2
…
5=FV-5
1=FV-1
2=FV-2
…
5=FV-5
1=R
2=R
3=R
4=L
5=L
1=D
2=U
3=U
4=D
5=U
RD.RU.RU.LD.LU
“juice”
Raw Accelerometer Data
Raw Accelerometer Data
Feature Matching
Labeled Dataset | Algorithm | Test Accuracy (%)
L/R | AdaBoost (RandomForests) | 68.67
 | AdaBoost (DecisionStumps) | 69.82
 | Neural Networks | 68.10
U/D | AdaBoost (RandomForests) | 56.60
 | AdaBoost (DecisionStumps) | 58.68
 | Neural Networks | 58.62
Triads | AdaBoost (RandomForests) | 16.37
 | AdaBoost (DecisionStumps) | 13.21
 | Neural Networks | 14.65
# errors (L/R, U/D) | Recovered Words Accuracy (%)
0 | 5.46
1 | 23.41
2 | 41.64
3 | 70.31
4 | 85.67
5 | 94.54
6 | 97.27
Recorded 1000 data points in 40 sessions with 25 letters in each sessions.
Sampled vibration signals for letters ‘a’ and ‘b’ are quite distinct
  Letter ‘a’ consists of one peak while letter ‘b’ is consist of three
Dataset Overview
Provides coarse grained labeling compared to exact alphabet labeling
  Letters on the left side of and including T, G, B – Left (L)
  Letter in the top row – Up (U)
  Adjacent keys grouped into triples
Left(L)/Right(R), Up(U)/Down(D) and Triads
Sample vibration signal for the word “juice”
  Shows distinct peaks for each letter
  Clipper module removes the beginning and ending noise
SignalBreaker module breaks the word signal into individual letters
Predictions made by the classifier are matched against a dictionary
  Used Harvard sentences as the candidate dictionary
  Labeled dictionary using L/R and U/D labels
  Hamming distance with each dictionary word is computed
  Output dictionary words with lowest Hamming distance
Example