## Slide 1
Smartphone accelerometers do not require explicit user permissions
Smartphones are often placed next to the user’s laptop or keyboard
Malicious applications can recover text by identifying signals from different keystrokes
Threat Model
Develop an infrastructure for characterizing keypress vibrations
  Captured, analyzed and built profiles of keypresses on a nearby keyboard based on the generated vibrations
  Successfully recovered words using Boosted Decision Stumps
Dataset made publicly available
  Provided noise-free signal data for each letter of the English alphabet
  Developed an infrastructure for analysis and extraction of features
Contributions
Input: A sentence from the Harvard dictionary
Output: All candidate words that constitute this sentence
  Exact matches are shown without other candidates
  Partial matches shown with lowest Hamming distanced words
EavesDroid is able to recover 1-3 lettered words (such as ‘box’, ‘key’, ‘in’) while Marquardt et. al work relies on human identification
Features extracted
  mean, rms, skewness, kurtosis, variance, min, max
  Fast Fourier Transformation coefficients (30)
Classifier used: AdaBoost with Decision Stump as weak learner
Data Processing Architecture
Experimentation
AdaBoost + Decision Stump achieves comparable accuracy with AdaBoost + Random Forests and Neural Networks.
By the principle of Occam’s Razor, we chose AdaBoost + Decision Stump as the classifier of EavesDroid
Challenges and Future Work
Number of candidate words increases along with dictionary size
  Leads to additional work in contextual identification
  Reducing search space is a possible solution (grouping letters into triads)
Accelerometer is extremely sensitive to surrounding noises
  Better signal filtering techniques required
  With advanced signal filtering techniques profiling of consecutive key presses into the model
Clustering on the letters’ signals and labeling them based on the frequency of each letter’s average appearance
Building the model on a word’s signal instead of the letter’s signal might identify word signatures with greater accuracy
Princeton University
Jennifer Guo Yi-Hsien Lin Akshay Mittal Wathsala Vithanage
EavesDroid: Keystroke recovery using mobile phone
accelerometers
Clipper
Signal Breaker
Feature Extractor
Supervised Learning Module
Labeled
Features
AdaBoost With Decision Stump
Labeler
Clipper
Signal Breaker
Feature Extractor
Features
Trained AdaBoost With Decision Stump
Dictionary With Keyboard Features
(L/R) (U/D)
Prediction Output
Learning Phase
Attack Phase
Phone
Feature Extractor
Keystrokes
L/R Classifier
U/R Classifier
Word Profile
Feature Matching
Word
Dictionary
“juice”
1=<x,y,z>
2=<x,y,z>
…
5=<x,y,z>
1=FV-1
2=FV-2
…
5=FV-5
1=FV-1
2=FV-2
…
5=FV-5
1=FV-1
2=FV-2
…
5=FV-5
1=R
2=R
3=R
4=L
5=L
1=D
2=U
3=U
4=D
5=U
RD.RU.RU.LD.LU
“juice”
Raw Accelerometer Data
Raw Accelerometer Data
Feature Matching
Labeled Dataset | Algorithm | Test Accuracy (%)
L/R | AdaBoost (RandomForests) | 68.67
 | AdaBoost (DecisionStumps) | 69.82
 | Neural Networks | 68.10
U/D | AdaBoost (RandomForests) | 56.60
 | AdaBoost (DecisionStumps) | 58.68
 | Neural Networks | 58.62
Triads | AdaBoost (RandomForests) | 16.37
 | AdaBoost (DecisionStumps) | 13.21
 | Neural Networks | 14.65
# labeling errors (L/R, U/D) | Recovered Words Accuracy (%)
0 | 5.46
1 | 23.41
2 | 41.64
3 | 70.31
4 | 85.67
5 | 94.54
6 | 97.27
Recorded 1000 data points in 40 sessions with 25 letters in each sessions.
Sampled vibration signals for letters ‘a’ and ‘b’ are quite distinct
  Letter ‘a’ consists of one peak while letter ‘b’ is consist of three
Dataset Overview
Provides coarse grained labeling compared to exact alphabet labeling
  Letters on the left side of and including T, G, B – Left (L)
  Letter in the top row – Up (U)
  Adjacent keys grouped into triples
Left(L)/Right(R), Up(U)/Down(D) and Triads
Sample vibration signal for the word “juice”
  Shows distinct peaks for each letter
  Clipper module removes the beginning and ending noise
SignalBreaker module breaks the word signal into individual letters
Predictions made by the classifier are matched against a dictionary
  Used Harvard sentences as the candidate dictionary
  Labeled dictionary using L/R and U/D labels
  Each n-letter word gets 2n-labels
  Hamming distance with each dictionary word is computed
  Output dictionary words with lowest Hamming distance
Example
Data set = Training set (66%) TR + Test set (33%) TE
  Prediction model built using TR
Experiment 1: 72 sets of Harvard sentences (4490 words)
  Represents words using individual letter signals from TE
  Among 4490 words
    85.67% have less than 5 labeling errors
Experiment 2: New York Times article (138 dictionary words + 257 new words)
  121 out of 138 dictionary words have less than 5 labeling errors
  This demonstrates practical applications of EavesDroid
Conclusion
Provide a simple model based on AdaBoost + Decision Stump and achieve comparable accuracies to a Neural Network based model used by Marquardt et. al